## Slide 1
Priest Lake Dam Operations Overview
Michelle Richman
June 3, 2025

## Slide 2: Purpose – To Discuss:
How dam operation decisions are made
How to manage the river and lake as a system
Data gaps
FAQs

## Slide 3: Topics
Context
Goal – Strike a balance
Framework for decisions
Seasonal operations

## Slide 4: Framework for Dam Operation Decisions
Written Guidance
Stakeholder Input
Natural Inputs
Basin Characteristics
Monitoring Information
Physical Configuration of the Dam

## Slide 5: Overarching Guidance - Idaho Code §70-507
Recreation Season
  Wet to normal years – 3.0 feet
  Dry to very dry – 3.0 to 3.5 feet
Fall Release
  After close of main recreation season
  Not below 0.1 feet
Lake & Quantity-focused

## Slide 6: Supporting Guidance
Priest River Basin Plan – 1995, 2003
Minimum Stream Flow Water Right - 1997 8/1 – 10/31: 300 cfs
Stakeholder Input
  Lower Priest River Instream Flow Study ~ IF&G
Governor’s WR – 800,000 AF – 1927
Historic agreements

## Slide 7: Natural Inputs, Basin Characteristics
Tributaries & Thorofare
Weather
Collaboration

## Slide 8: Monitoring Information - Spring
NRCS SNOTEL
NRCS Water Supply Forecasts
Drought Monitor

## Slide 9: Monitoring Information – Year-round
USGS Stations (3)
USGS Priest River nr Coolin

## Slide 10: Spring – Dam Operations
First Decision
  Catch from peak
  Bring lake level up

## Slide 11: Spring – Type of Year
  Dry vs. Wet
  Determines lake level
    Wet – 3.0 feet
    Dry – 3.0 to 3.5 feet

## Slide 12: Spring – Daily Operations
G
Hold lake at a specified level
Match estimated inflow
  Hydrology calculation
  Granite Creek calculation
Rapidly falling inflow – 2021
2500 cfs, early June
200 cfs, early July

## Slide 13: Gate Change Calculation
Dynamic system – hours to days lag in response

## Slide 14: Summer Operations
Held at 3.0 feet 1951 to 2022
Last 3 years
  2022
  2023
  2024
6-inch Radial Gate Extension

## Slide 15: Summer – 2015
USGS Flow Measurements August 4-5, 2015
  Inflowing Tributaries = 118.5 cfs
  Thorofare = -175 cfs
  Combined = -56.5 cfs
OUTFLOW from DAM 44.6 cfs
Net outflow = 101 cfs
Collaboration

## Slide 16: Summer - 2022
Hold lake at ~3.2’
Takeaways – river fluctuation when hold lake level constant

## Slide 17: Summer - 2023
Hold river at 184 cfs, (7/26-9/1)
Takeaways – Priest River Flow down to 230 cfs

## Slide 18: Summer - 2024
Hold lake at 3.43 ft, then release to 3.0
Takeaway – slow the release down to bring lake to 3.0 ft by 9/30

## Slide 19: Supporting Guidance
IF&G
  200 cfs minimum from 8/1 to 10/31
  400 cfs ideal
IWRB
  MSF 300 cfs (8/1 to 10/31)

## Slide 20: 2017
Sustained low flow
Volume Deficit
Target Flow Rate

## Slide 21: Targets
2017
Chart: 2017
| 150 cfs Target | 175 cfs Target | 185 cfs Target | 200 cfs Target
2017 | 3.27 | 3.39 | 3.44 | 3.51

## Slide 22: Targets
Average of 2017-2021
Why not 400 cfs?
Chart: Average 2017-2021
| 150 cfs Target | 175 cfs Target | 185 cfs Target | 200 cfs Target
Average | 3.18 | 3.274 | 3.314 | 3.378

## Slide 23: Recommended Best Practices – Dry Years
Hold lake to 3.31-3.44 feet
Target flow rate of 200 cfs
Flow will fall below target in some dry years
Wet years – no change

## Slide 24: Dates Flow Drops
Target Flow: 200 cfs
Chart: 
| 2017 | 2018 | 2019 | 2020 | 2021 | Average
# Days to Septmeber 30 | 58 | 52 | 51 | 48 | 84 | 58.6
Date Drop Below 200 cfs | 
2017 | 8/3/2017
2018 | 8/9/2018
2019 | 8/10/2019
2020 | 8/13/2020
2021 | 7/8/2021

## Slide 25: Target Flow & Lake Level Calculations
The following shows a sample calculation to reach the values in Table 8 above. Assume the base flow rate dropped to 97 cfs for 60 days. The flow augmentation would be 88 cfs to bring the flow back up to 185 cfs. needed for flow augmentation The volume deficit for the target flow of 185 cfs for 60 days is: And the associated lake level increase is: Therefore, the lake level during the recreation season would need to be held at: Lake level = 3.0 feet + 0.44 feet = approximately 3.44 feet
For target flow = 200 cfs: Assume the base flow rate dropped to 125 cfs for 60 days. needed for flow augmentation The volume deficit for the target flow of 200 cfs for 60 days is: And the associated lake level increase is: Lake level = 3.0 feet + 0.38 feet = approximately 3.38 feet Dividing .38 by 60, the lake can drop 0.006 ft/day or 0.04 ft/week through September 30th.

## Slide 26: End of Summer vs Spring Volumes

## Slide 27: Fall Release supporting Guidance
Statute: Close of main recreation season
IF&G: Complete by Nov. 1
IF&G: >600 cfs, negative impact IF&G: 1000 cfs max
Photo – Craig Hill, Nov. 12, 2019

## Slide 28: Fall Release Past Practices
WWP/Avista operated for water releases in Fall for downstream power production
Incrementally open gates
Lake drains
Flow exceeded 2000 cfs

## Slide 29: Fall Release Best Practices
No current agreements for power production = opportunity
Incrementally open gates on Oct. 1
Cap at 1000 cfs
Instead of dropping 3 feet, lake drops 2 feet
To ~1.0 foot by Nov. 1 & Hold
Leaves room for spring runoff

## Slide 30: Fall Release Best Practices
Cap at 1000 cfs

## Slide 31: Next Steps
Data collection
Informed decisions
Stakeholder input
Communication

## Slide 32: Conclusions
Planning for the future
Striking a balance to manage the lake and river as a system

## Slide 33
Questions?
Michelle Richman northerninfo@idwr.Idaho.gov 208-762-2800

## Slide 34: Average River Flow Before & After Dam Built
Before dam Average flow met MSF water right in September
After dam Average flow did not meet MSF water right

## Slide 35: Average Lake Level Before & After Dam Built
Hydrograph – Lake
Chart: Priest Lake Daily Average Gage Height Before and After Dam Construction