## Slide 1
Priest Lake Dam 2025 Operations Overview
Michelle Richman Bill Cresse October 30, 2025

## Slide 2: Purpose – To Discuss:
Recreation Season 2025 Dam Operations
Fall Drawdown 2025 Stakeholder Feedback Monitoring Efforts Next Steps

## Slide 3: Lake Operations – Recreation Season - 2025
Idaho Code §70-507
Dry year
Maintain pool 3.0’-3.5’
Bring lake up to 3.0’ by Memorial Day

## Slide 4: Lake Level – Recreation Season - 2025
Peak: 3.8’ May 31st
Stabilized, 3.5’ by June 15th
3.35’ on August 4th
3.0’ October 1st

## Slide 5: Priest River – Recreation Season 2025
Peak: 3,820 CFS May 30th
300 CFS July 31st
200 CFS Minimum flow
Rain events
200 cfs minimum

## Slide 6: Evaluation – Recreation Season 2025
Functioned as planned
Sustained 200 cfs or more in Priest River through Sept. 30th
Higher lake level early in the recreation season – 3.4’
Rain helped

## Slide 7: Lake Operations – Fall Drawdown
Starting at 3.0’ by 10/1
Fall Drawdown 10/1 to 10/31
0.1’ minimum per §70-507
Complete by Nov. 1 for Kokanee

## Slide 8: Fall Drawdown – Historic Practices
Open the gates and drain the lake
*1,000 CFS in Priest River Basin Plan

## Slide 9: Historic Practice - Fall Drawdown - 2024
Increase the flow incrementally
Peak flow 2600 cfs+

## Slide 10: Fall Release Best Practices
Capped Flow
Capped flow
Original announcement: cap the flow at 1000 cfs, 1.0’ minimum lake level
Priest River Basin Plan

## Slide 11: Fall Drawdown – Stakeholder Feedback
Docks and infrastructure
Floating debris
Safety issues

## Slide 12: Gate Damage
Visible damage
Revised 2025 target to bring minimum lake below 1.0’
12
Damage

## Slide 13: Fall Drawdown – Revised Cap on Flow
2024 and 2025
comparison
1000 cfs maximum
1.0’ lake level
1500 cfs maximum
0.4’ lake level
Revised announcement
in September

## Slide 14: Fall Drawdown – Lake Level Comparison
2024 and 2025 comparison
Lake level 2.59’ on Oct 8
Extends recreation on the lake
More gradual change in lake level
Target 0.4’ by November 1st

## Slide 15: Benefits Current Drawdown Method Relative to Historic Practices
15
1,600
1,400
1,200
1,000
800
600
400
200
0
9/30/2025
10/2/2025
10/4/2025
10/6/2025
10/8/2025
10/10/2025
10/12/2025
10/14/2025
10/16/2025
10/18/2025
10/20/2025
10/22/2025
10/24/2025
10/26/2025
10/28/2025
10/30/2025
Priest Lake Drawdown
Outflow (cfs)
Gradual more predictable lake level reduction
Boats extra week on lake
Almost 2 full weeks high flow river recreation
Dam safety
Reduced flow rate in Priest River
Complete by Nov. 1st
Fish habitat (Kokanee)

## Slide 16: Best Practices
3.0’-3.5’ dry summer
Higher summer river flows
Limit changes to 20% of flow
Cap flow during drawdown
Drawdown done by Nov. 1st
Winter lake level > 0.1’
16

## Slide 17: Stakeholder Feedback
IDFG
Copper Bay Construction
Elkins Resort
Kayakers
Inland Northwest Fishing Guys
Lakes Commission
Priest River Watershed Group
Selkirk Conservation Alliance
IDEQ
IDOL
17
Lion Head Creek

## Slide 18: Operations – Feedback Loop
2025 operations are the beginning of an iterative process
Continue to gather feedback
IWRB stakeholder meeting
18

## Slide 19: Best Practices - Monitoring
19
Granite Creek looking downstream at Reeder Bay Road crossing
Monitor NOAA for Rain, Heat
Monitor USGS stage & flow
Monitor inflow - tributaries

## Slide 20: Inflow Monitoring
New monitoring sites
  New staff gage on Granite Creek
  New staff gage on Upper Priest River
  New pressure transducer planned for Hunt Creek
20

## Slide 21: Tributary Inflow Measurements
Difficult to manage gate operations without knowledge of tributary inflows, inflow quantities, and inflow timing
21
Hughes Fork just South of Gold Creek Road (NF-1013)

## Slide 22: Inflow Measurements (CFS)
Upper Priest River into Upper Priest Lake: 30.7 CFS

## Slide 23: Next Steps
Stakeholder feedback
Lessons learned
  Iterative process
  Applied to future operations
2026 operations
IWRB meeting

## Slide 24
Questions?
Michelle Richman Bill Cresse
northerninfo@idwr.Idaho.gov 208-762-2800

## Slide 25: Fall Release Best Practices
Cap at 1,500 CFS
2024
2025
Cap at 1,500 CFS

## Slide 26: Best Practices - Monitoring
Monitor NOAA for Rain, Heat
Monitor USGS stage & flow
Monitor staff gages
  Granite Creek (43%)

## Slide 27: Natural inputs
Rain storm Oct. 18-19
  Net zero (0) outflow
•
Qwerty

## Slide 28: Stakeholder Feedback
How do we decide appropriate actions?
  Example: IDFG 1,000 CFS max during drawdown (Kokanee)
    Discussed concept of mimicking nature with IDFG
      Gradual more predictable lake level reduction, that better mirrors natural drawdown, without sharp peaks in discharge from dam
    Need 1,500 CFS to get lake level down by 10/31
    Higher lake level associated with 1,000 CFS can create dam safety issue